## CPCD50 Forklift Truck

Features of the Diesel Forklift
1. State of the art appearance design; streamline, dynamic and stylish appearance. 
2. Large sized injection molded covering part makes the forklift truck more elegant and user friendly. 
3. Commonly used material handling machinery with long wheelbase design, ensuring higher longitudinal stability and higher lifting capacity; reduced load on the real axle extends steering wheel’s lifespan. 
4. In virtue of reduction of the whole machine size, our diesel forklift can dramatically increase warehouse use ratio. 
5. Japanese OKAMURA, NISSAN and Chinese HC transmissions are optional for the lift truck. They come with best in class structure and reliable performance. Among which, the OKAMURA type transmission features the state of the art floating structure, ensuring completely flexible connection between engine and forklift frame, thus minimizing machine vibration.

Technical Parameter

| General | 1 | Product name | Forklift truck |
| --- | --- | --- | --- |
|  | 2 | Basic model | - | CPCD50 |
|  | 3 | Type | - | RG41 | RW14 | RW14B | RW38 | RW38B | RW19A | RW28 |
|  | 4 | Power type | - | Diesel |
|  | 5 | Rated load | kg | 5000 |
|  | 6 | Load center distance | mm | 600 |
| Dimensions of Forklift Truck | 7 | Lifting height | mm | 3000 |
|  | 8 | Free lift height | mm | 160 |
|  | 9 | Fork size | L×W×T | mm | 1200×150×60 |
|  | 10 | Fork spacing (Outside) | Min./Max. | mm | 300/1700 |
|  | 11 | Mast tilt angle | F/R | degree | 6/12 |
|  | 12 | Fork overhang (Wheel center to fork surface) | mm | 595.5 |
|  | 13 | Overall dimensions | Length (To surface of fork) |  | 3510 | 3460 | 3510 |
|  | 14 |  | Overall width | mm | 1990 |
|  | 15 |  | Mast closed height | mm | 2500 |
|  | 16 |  | Mast extended height | mm | 4420 |
|  | 17 |  | Overhead guard height | mm | 2340(2370*) |
|  | 18 | Turning radius (Outside) | mm | 3210 | 3160 | 3210 |
|  | 19 | Min. width of right angle aisle | mm | 2830 | 2780 | 2830 |
|  | 20 | Min. width of right angle stacking aisle (Including load length and clearance) | mm | 3820 | 3770 | 3820 |
| Performance of Forklift Truck | 21 | Speed | Travel speed | km/h | 26 | 23 | 26 | 23 | 26 | 29 | 22 |
|  | 22 |  | Lifting speed (Full load) | mm/sec | 405 | 405 | 406 | 410 | 405 |
|  | 23 | Max. gradeability (Full load) | % | 20 |
|  | 24 | Dead weight | kg | 8000 |
| Wheel & Tire | 25 | Tyre | Front | mm | 8.25-15-14PR |
|  | 26 |  | Rear | mm | 8.25-15-14PR |
|  | 27 | Tread | Front/Rear | mm | 1489/1460 |
|  | 28 | Wheelbase | mm | 2300 | 2250 | - | 2300 |
|  | 29 | Ground clearance | mm | 170 |
|  | 30 | Battery | Voltage/Capacity (5HR) | V/AH | 2×12/90 |
| Power & Transmission of Forklift Truck | 31 | Engine | Model | - | YC4A115Z | 6BG1QP | QSB3.3 | TD42AA | QSB4.5 |
|  | 32 |  | Manufacturer | - | CHINA,YUCHAI | ISUZU | CUMMINS | UD | CUMMINS |
|  | 33 |  | Rated output/rpm | kW | 85/2200 | 84.6/2200 | 74/2200 | 59/2300 | 82/2200 |
|  | 34 |  | Rated torque/rpm | N.m | 425/1500 | 411/1500 | 415/1600 | 254/1800 | 488/1500 |
|  | 35 |  | Quantity of cylinder |  | 4 | 6 | 4 | 6 | 4 |
|  | 36 |  | Bore×stroke | mm | 108×130 | 105×125 | 95×115 | 96×96 | 107×124 |
|  | 37 |  | Emission standard | - | - | - | Stage IIIA/Tier3 | - | Stage IIIA/Tier3 |
|  | 38 |  | Displacement | cc | 4836 | 6494 | 3300 | 4169 | 4460 |
|  | 39 | Transmissions | Fuel tank capacity | L | 120 |
|  | 40 |  | Manufacturer | - | CHINA | CHINA | OKAMURA | CHINA | OKAMURA | NISSAN | CHINA |
|  | 41 |  | Type | - | Power shift |
|  | 42 |  | Gear | Forward/reverse | - | 2/2 | 1/1 | 2/2 | 1/1 | 1/1 | 1/1 | 2/2 |
| Others | 43 | Operating pressure | For attachment | MPa | 19 |
| 1. The lifting height of the forklift truck can be customized based on customer demand. 2. Attachment is available with this heavy duty forklift. 3. Data in the table is for standard fork lift only. Customer is welcomed to contact us for more detail. 4. All specifications for the material handling equipment are subject to change without prior notice. |