## CPCD80 Forklift Truck

Features of the Diesel Forklift
1. The CPCD80 series forklift comes with the latest appearance design. It has a great line, dynamic and stylish appearance. 
2. Thanks to a large sized injection molded covering part, the forklift truck looks more elegant and user friendly. 
3. Long wheelbase design ensures higher longitudinal stability and higher lifting capacity. Load on the real axle is reduced, extending the service life of steering wheel. 
4. Due to the reduction of machine size, our diesel forklift has smaller turning radius and narrows the passage for right angle stacking, thus considerably improving warehouse use ratio and providing suitability for use in containers. 
5. Japanese OKAMURA, NISSAN and Chinese HC transmissions are optional for the lift truck. They come with best in class structure and reliable performance. The OKAMURA type transmission features floating structure, ensuring a completely flexible connection between engine and forklift frame, thus minimizing machine vibration.

Technical Parameter

| General | 1 | Product name | Forklift truck |
| --- | --- | --- | --- |
|  | 2 | Basic model | - | CPCD80 |
|  | 3 | Type | - | RG16 | RG17 | RG25 | RW14 | RW28 |
|  | 4 | Power type | - | Diesel | Diesel | Diesel | Diesel | Diesel |
|  | 5 | Rated load | kg | 8000 | 8000 | 8000 | 8000 | 8000 |
|  | 6 | Load center distance | mm | 600 | 600 | 600 | 600 | 600 |
| Characteristics & Dimensions of Forklift Truck | 7 | Lifting height | mm | 3000 | 3000 | 3000 | 3000 | 3000 |
|  | 8 | Free lift height | mm | 200 | 200 | 200 | 200 | 200 |
|  | 9 | Fork size | L×W×T | mm | 1500×160×75 | 1500×160×75 | 1500×160×75 | 1500×160×75 | 1500×160×75 |
|  | 10 | Fork spacing (Outside) | Min./Max. | mm | 440×1950 | 440×1950 | 440×1950 | 440×1950 | 440×1950 |
|  | 11 | Mast tilt range | F/R | degree | 6/12 | 6/12 | 6/12 | 6/12 | 6/12 |
|  | 12 | Fork overhang (Wheel center to fork surface) | mm | 705 | 705 | 705 | 705 | 705 |
|  | 13 | Overall dimensions | Length (To surface of fork) | mm | 3896 | 3896 | 3896 | 3896 | 3896 |
|  | 14 |  | Overall width | mm | 2165 | 2165 | 2165 | 2165 | 2165 |
|  | 15 |  | Mast closed height | mm | 2700 | 2700 | 2700 | 2700 | 2700 |
|  | 16 |  | Mast extended height | mm | 4510 | 4510 | 4510 | 4510 | 4510 |
|  | 17 |  | Overhead guard height | mm | 2540(2570*) | 2540(2570*) | 2540(2570*) | 2540(2570*) | 2540(2570*) |
|  | 18 | Turning radius (Outside) | mm | 3690 | 3690 | 3690 | 3690 | 3690 |
|  | 19 | Min. width of right angle stacking aisle | mm | 3300 | 3300 | 3300 | 3300 | 3300 |
|  | 20 | Min. width of right angle stacking aisle (Including load length and clearance) | mm | 6095 | 6095 | 6095 | 6095 | 6095 |
| Performance of Forklift Truck | 21 | Speed | Travel speed | km/h | 0-26 | 0-26 | 0-26 | 0-26 | 0-26 |
|  | 22 |  | Lifting speed (Full load) | mm/sec | 320 | 380 | 380 | 380 | 380 |
|  | 23 | Max. gradeability (Full load) | % | 20 | 20 | 20 | 20 | 20 |
|  | 24 | Dead weight | kg | 11300 | 11300 | 11300 | 11300 | 11300 |
| Wheel& tires | 25 | Tyre | Front | mm | 9.00-20-14PR | 9.00-20-14PR | 9.00-20-14PR | 9.00-20-14PR | 9.00-20-14PR |
|  | 26 |  | Rear | mm | 9.00-20-14PR | 9.00-20-14PR | 9.00-20-14PR | 9.00-20-14PR | 9.00-20-14PR |
|  | 27 | Tread | Front/Rear | mm | 1600/1700 | 1600/1700 | 1600/1700 | 1600/1700 | 1600/1700 |
|  | 28 | Wheelbase | mm | 2500 | 2500 | 2500 | 2500 | 2500 |
|  | 29 | Ground clearance | mm | 250 | 250 | 250 | 250 | 250 |
|  | 30 | Battery | Voltage/Capacity (5HR) | V/Ah | 2×12/90 | 2×12/90 | 2×12/90 | 2×12/90 | 2×12/90 |
| Power & Transmission of Forklift Truck | 31 | Engine | Model | - | CY6102BG | YC6B125 | LR6M3 | 6BG1QP | QSB4.5 |
|  | 32 |  | Manufacturer | - | CHINA | CHINA | CHINA | ISUZU | CUMMINS |
|  | 33 |  | Rated output/rpm | kW | 81/2500 | 92/2200 | 92/2200 | 84.6/2200 | 82/2200 |
|  | 34 |  | Rated torque/rpm | N.m | 353/1700 | 463/1400-1700 | 450/1400-1600 | 411/1400-1600 | 488/1500 |
|  | 35 |  | Quantity of cylinder | - | 6 | 6 | 6 | 6 | 4 |
|  | 36 |  | Bore×stroke | mm | 102×118 | 108×125 | 110×125 | 105×125 | 107×124 |
|  | 37 |  | Emission standard | - | - | - | - | - | Stage IIIA/Tier3 |
|  | 38 |  | Displacement | cc | 5785 | 6871 | 7120 | 6494 | 4460 |
|  | 39 | Transmissions | Fuel tank capacity | L | 120 | 120 | 120 | 120 | 120 |
|  | 40 |  | Manufacturer | - | CHINA | CHINA | CHINA | CHINA | CHINA |
|  | 41 |  | Type | - | Power shift | Power shift | Power shift | Power shift | Power shift |
|  | 42 |  | Gear | Forward-reverse | - | 2/2 | 2/2 | 2/2 | 2/2 | 2/2 |
| Others | 43 | Operating pressure | For attachment | MPa | 19.5 | 19.5 | 19.5 | 19.5 | 19.5 |
| 1. Bespoke lifting height available. 2. This range of material handling equipment can be provided with attachment. 3. Data in the table is for standard model only. For further information, please contact us. 4. All specifications are subject to change without prior notice. |

Related Names
China Forklift Truck Exporter︱Powered Industrial Truck︱Warehouse Truck