## 8125HL Double Steel Drum Hydraulic Vibrating Road Roller

This 8125HL double steel drum hydraulic vibrating road roller adopts the international advanced technology and its key components are imported from abroad. This machine is mainly applied into the pavement engineering for compacting various materials such as stabilized soil, asphalt concrete and hard concrete. It is also suitable for the subgrade works and is an ideal compacting machine for building high-grade highway, railway, airport, dam, municipal roads and industrial ground.

Main Features
1. The 8125HL road roller adopts Cummins B series water-cooled diesel engine with high coefficient of power reserve. 
2. The hydrostatic and all-wheel drive system is driven by hydraulic motor, with two-gear continuously variable speed. 
3. Dual frequency and amplitudes vibration device comes with imported plunger pumps and motors. 
4. Articulated steering mechanism and unique crab walk type travel mechanism deliver high flexibility and maneuverability. 
5. Built-in wet type multiple-disc brake is used to brake in emergency circumstances by fuel cut-off, which greatly improves the operation safety and reliability. 
6. The whole construction machine comes with a striking appearance in streamline design. The front preposed control board offers a great vision. 
7. You can enjoy driving in the spacious and comfortable cab that is equipped with double steering wheels and seats for convenient operation. 
8. Electrically controlled water spraying system of the road roller comes with a large capacity FRP water tank.

| Model |  | LDD212H |
| --- | --- | --- |
| Operating mass | kg | 12000 |
| Static Linear Load | N/cm | 282 |
| Amplitude | mm | 0.74/0.35 |
| Vibration Frequency | Hz | 40/50 |
| Centrifugal force | KN | 150×2/99×2 |
| Max. Traveling Speed | km/h | 13 |
| Grade Ability | % | 40 |
| Turning Radius | mm | 7000 |
| Vibration Drum Width | mm | 2130 |
| Vibration Drum Diameter | mm | 1350 |
| Wheel Base | mm | 3440 |
| Min. Ground Clearance | mm | 350 |
| Diesel Engine Model |  | Cummins4BTA3.9 |
| Diesel Engine Power | kW | 93 |
| Dimension | mm | 5360×2270×2970 |