## 8125L Double Steel Drum Vibratory Road Roller

This machine is also named tandem vibratory roller which is developed by our company. It is configured with one good power performance engine and two 1700mm wide compaction drums. This kind of road roller features low emission, large power conservation capacity, high working efficiency, as well as novelty.

Main Features
1. The 8125L series road roller travels by means of side drive of gears, featured with hydraulic vibration, hydraulic steeing, three gear speeds and easy transfer to other construction sites. 
2. It is deisgned with double steering wheels and double seats, providing an excellent vision for side compaction. 
3. The tandem vibratory roller adopts Commins engine that comes with strong driving force, low oil comsumption, standard emission, and great starting performance. 
4. The roller comes with an electrically controlled water sparying unit for front and rear drums.

| Operating mass | 12000kg |
| --- | --- |
| Exciting force | 120kN |
| Vibration frequency | 50Hz |
| Vibration amplitude | 0.35mm |
| Traveling speed | 2.5km/h 5.5km/h 8km/h |
| Grade ability | 20% |
| Dimension | 5390×2060×2980mm |
| Engine model | 4BT3.9-C80 |
| Engine power | 60kW |
| Min turning radius | 7000mm |
| Drum width | 1700mm |
| Min ground clearance | 310mm |
| Sprinkler tank capacity | 280L+280L |