## 8065L Double Steel Drum Vibrating Road Roller

Feature
1. This 8065L double steel drum vibrating road roller features compact structure, reasonable layout, and attractive appearance. 
2. The front drum runs by the hydraulic vibration while the rear wheel is driven by the mechanical drive. 
3. Our road roller adopts the ZN490Q engine manufactured by Changchai Co., Ltd. The Changchai engine has excellent performance and is easy to start. 
4. The rear drum runs driven by the gear drive in a safe and reliable way.
5. It is very convenient for the maintenance of the whole machine. 
6. This engineering vehicle can be flexibly operated with the hydraulic central articulated steering device. 
7. The driving cab adopts the standard umbrella structure. It is your decision to install this umbrella or not.

Technical Parameter

| Operating mass | kg | 6000 |
| --- | --- | --- |
| Driving drum distributed weight | kg | 3600 |
| Vibration drum distributed weight | kg | 2400 |
| Static linear load of driving wheel | N/cm | 288 |
| Static linear load of vibration wheel | N/cm | 192 |
| Bus load of vibration wheel | N/cm | 672 |
| Centrifugal force | KN | 60 |
| Vibration frequency | HZ | 50 |
| Theoretical value of amplitude | mm | 0.5 |
| Dimension (L×W×H) | mm | 3460×1480×2730 |
| Wheel base | mm | 2479 |
| Min. ground clearance | mm | 386 |
| Min. turning radius (outside) | mm | ≤6000 |
| Compaction width | mm | 1250 |
| Grade ability | % | 20 |
| Vibration drum diameter | mm | 950 |
| Vibration drum width | mm | 1250 |
| The first speed | km/h | 2.5 |
| The second speed | km/h | 7 |
| Engine model |  | Changchai ZN490Q (vertical water-cooling four-stroke) |
| Rated power | kw | 33.5 |
| Rated rotate speed | r/min | 2600 |
| Water tank capacity | L | 180 |