## 8035L Road Roller

Main Features 
1. Powered by ZN385Q/ZN390Q diesel engine, the road roller comes with excellent starting performance. 
2. The rear drum is driven by the gear rotation and the front drum runs by vibration. 
3. The front and rear bodies are connected with hinge, which facilitates the power-assisted steering. 
4. Compaction height is over 600mm. 
5. The gear box made using Japanese technology enables easy gear control. Three gears ensure perfect Compaction effect and easy transition. 
6. Platform trailer is available. 
7. The road roller has obtained two national patents.

Technical Parameter

| Operating mass | 3000kg |
| --- | --- |
| Centrifugal force | 32kN |
| Vibration frequency | 50Hz |
| Vibration amplitude | 0.5mm |
| Traveling speed | 2.5km/h 5.2km/h 8km/h |
| Grade ability | 20% |
| Dimension | 2880×1280×2650mm |
| Engine model | ZN385Q |
| Engine power | 22kW |
| Turning radius | 4500mm |
| Drum width | 1100mm |
| Wheel base | 2050mm |
| Water tank capacity | 100L |