## Motor Grader 722H

1. Our 722H motor grader adopts ShangChai engine with model SC11CB220G2B1. 
2. The adopted hydraulic system can achieve efficient control over every working part.
3. The 6 forward and 3 reverse power-shift transmission features sing-handle and electro-hydraulic control, and ensures simple and convenient operation. 
4. It is available with the hydraulic lock and auto lock/unlock NO-SPIN differential, providing stability and powerful traction. 
5. Designed with perfect axel load allocation, the motor grader is applicable to hard surface cutting with excellent stability.
6. When combined with box-typed frame, the transmission system allows the vehicle to complete heavy-duty work.
7. The machinery is equipped with flexible blade suspension system and articulated frame, making it enjoy a wide working range.

Specifications of Motor Grader

| Overall Dimension |
| --- |
| 1 | Length | 9235mm |
| 2 | Width | 4320mm |
| 3 | Height(To the top of the cab) | 3370mm |
| 4 | Wheel base | 6100mm |
| 5 | Tread | 2120(mm) |
| Main Technical Specification |
| 1 | Operating weight | 16100kg |
| 2 | Blade length | 4320mm |
| 3 | Blade height | 545mm |
| 4 | Shovel Blade thickness | 16mm |
| 5 | Max lifting height | 450mm |
| 6 | Max grading depth | 535mm |
| 7 | Min. turning radius | 7400mm |
| 8 | Pivot angle frame | +26° |
| 9 | Max turning angle(front wheel) | +49° |
| 10 | Oscillating angle of front axle | 32° |
| 11 | Min ground clearance | 430mm |
| 12 | Cut angle | 29-77° |
| 13 | Traveling speed(Km/h),6 forward and 3 reverse |
|  | (1) Ⅰ gear forward | 6.8 |  |
|  | (2) Ⅱ gear forward | 10.3 |  |
|  | (3) Ⅲ gear forward | 15.3 |  |
|  | (4) Ⅳ gear forward | 22.7 |  |
|  | (5) Ⅴ gear forward | 32 |  |
|  | (6) Ⅵ gear forward | 47 |  |
|  | (7) Ⅰ gear reverse | 6.8 |  |
|  | (8) Ⅱ gear reverse | 15.3 |  |
|  | (9) Ⅲ gear reverse | 32 |  |
| Diesel Engine |  |
| 1 | Model | ShangChai SC11CB220G2B1 engine |  |
| 2 | Type | Direct injection. Turbocharged. Water cooling |  |
| 3 | Rated output | 162 kW |  |
| 4 | Inter-bore of cylinder/Stroke | 121/152 (mm) |  |
| 5 | Total exhaust of cylinder | 10.49 (L) |  |
| 6 | Model of starting motor | KB-24V |  |
| 7 | Power of start motor | 7.5(KW) |  |
| 8 | Voltage of starting motor | 24(V) |  |
| 9 | Rated speed | 2200(r/min) |  |
| 10 | Max. Torque | 823±6%(N.m)/(1400r/min) |  |
| 11 | Starting type | Electric |  |
| 12 | Min. specific fuel consumption | <235(g/Kw.h) |  |
| 13 | Engine specific oil consumption | 0.7(g/Kw.h) |  |
| 14 | Net weight | 960(kg) |  |
| Transmission System |  |
| 1. Torque Converter |  |
| 1 | Model | WG200(ZF) |  |
| 2 | Type | 3-elements.single stage |  |
| 3 | Torque ratio | 2.55 |  |
| 4 | Cooling type | Pressure oil circulating |  |
| 2. Transmission Case |  |
| 1 | Model | WG200(ZF) |  |
| 2 | Type | power shift, single-shift lever, netural-shift lock device |  |
| 3 | Gear shift position | 6 Forward and 3 reverse gears |  |
| 3. Axle and Tire |  |
| 1 | Type of main reducer | spiral bevel gear, single stage |  |
| 2 | Gear ratio of main reducer | 3.583 |  |
| 3 | Type of final reducer | Single stage chain-drive |  |
| 4 | Gear of ratio of final reducer | 3.75 |  |
| 5 | Gear ratio | 13.436 |  |
| 6 | Max. drawing force | 87.4KN |  |
| 7 | Tandem drive | Double row roller-chains |  |
| 8 | Size of tire | 17.5-25-14PR(standard) 14.00-24-16PR(optional) |  |
| Working Device Hydraulic System |  |
| 1 | Model of oil pump(include steering pump) | CBGj2045/1025 |  |
| 2 | System pressure | 175(kgf/cm2) |  |
| 3 | Model of distribution valve | HUSCO5000-D |  |
| 4 | Hydraulic lock | KAYABA technology |  |
| 5 | Model of oil motor | EATON, JS-130 |  |
| Steering System |  |
| 1 | Type | Fore Tire deflexion |  |
| 2 | Model of steering gear | BZZ1-E160B+FKA-163022 |  |
| 3 | System pressure | 16MPa |  |
| Brake System |  |
| 1 | Type of traveling brake | Hydraulic assisted and inner-expanding brake |  |
| 2 | System pressure | 100(kgf/cm2) |  |
| 3 | Type of parking brake | Mechanical and inner-expanding brake |  |
| Oil Capacity |  |
| 1 | Fuel(diesel) | 378L |  |
| 2 | Engine lubricating oil | 24L |  |
| 3 | Oil for converter and gear box | 28L |  |
| 4 | Oil for hydraulic system | 117L |  |
| 5 | Oil for driving rear axles | 18L |  |
| 6 | Tandem box | 90L |  |