## Road Roller 8202-5

Our 8202-5 road roller is widely used to compact asphalt surface, cohesive or non-cohesive base layers, as well as sub-base layers of various materials. It is characterized by eleven-wheel oscillation, ensuring good compacting effect. In addition, this pneumatic roller utilizes dual sprinkler systems with large ballast capacity. Moreover, the ground pressure can be well adjusted to meet different road construction requirements.

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length | 5060mm |
| 2 | Width | 2381mm |
| 3 | Height(To the top of the cab) | 3456mm |
| 4 | Wheel base | 3840mm |
| Main Technical Specification |
| 1 | Max Operating weight | 20000kg |
| 2 | Min Operating weight | 11800kg |
| 3 | Max. ballast water | 2300 kg |
| 4 | Average ground press | 235-395kPa |
| 5 | Min. ground clearance | 270mm |
| 6 | Roller width | 2250mm |
| 7 | Gradeability | ≥20% |
| 8 | Min. turning radius(Outside of rear wheel) | ≤8000mm |
| 9 | Traveling speed(Km/h),2 forward and 2 reverse |
|  | (1) 1st gear forward | 0~8 |
|  | (2) 2nd gear forward | 0~16 |
|  | (3) 1st gear reverse | 0~8 |
|  | (4) 2nd gear reverse | 0~16 |
| Diesel Engine |
| 1 | Model | Chinese Engine YC6B120-T20 |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 85 kW |
| 4 | Rated speed | 2000(r/min) |
| 5 | Inter-bore of cylinder/stroke | 6-108×125 (mm) |
| 6 | Total exhaust of cylinder | 6.87 (L) |
| 7 | Max. Torque | 450 (N.M) |
| 8 | Min. specific fuel consumption | 240(g/Kw.h) |
| 9 | Model and parameter of starting motor | 6.6kW-24V |
| 10 | Starting type | Electric |
| 11 | Net weight | 680(kg) |
| Transmission System |
| 1. Torque Converter |
| 1 | Model | YD15 |
| 2 | Type | 3-elements.single stage |
| 3 | Torque ratio | 2.52 |
| 4 | Cooling type | Pressure oil circulating |
| 5 | Type | Power shift, spur gear constant mesh |
| 6 | Gear shift position | 2 Forward and 2 reverse gears |
| 2. Axle and Tire |
| 1 | Type of main reducer | spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 5.286 |
| 3 | Type of final reducer | Single stage, chain driven |
| 4 | Chain-Gear of ratio of final reducer | 2.462 |
| 5 | total ratios | 13.01 |
| 6 | Size of tire | 11.00-20-16PRC-1A |
| 7 | Number of tire | Front 5&Rear6 |
| Steering System |
| 1 | Type | Tire deflexion full hydraulic steering system |
| 2 | Model of steering gear | Bzz1-E500C |
| 3 | System pressure | 14MPa |
| 4 | Dimension of steering cylinder | Ф90x45x296(mm) |
| Brake System |
| 1 | Type of traveling brake | Air-over-hydraulic activate drum brake of 4 rear wheel |
| 2 | Air pressure | 7-8(kgf/cm2) |
| 3 | Type of parking brake | Band brake Manual control cutting-off air brake |
| Oil Capacity |
| 1 | Fuel(diesel) | 125L |
| 2 | Engine lubricating oil | 15 L |
| 3 | Oil for converter and gear box | 20 L |
| 4 | Oil for hydraulic system | 55L |
| 5 | Oil for driving axles(F/R) | 15 L |