## Road Roller YZ12H with Rexroth

Structures of Road Roller YZ12H with Rexroth :
1. Road Roller YZ12H with Rexroth is equipped with DongFeng Cummins engine,
2. Single frequency & Double amplitude and super centrifugal force creates strong compacting effect
3. Rear-wheel hydraulic drive and stepless T/M.

Features of Road Roller YZ12H with Rexroth :
1. Reasonable configuration, reliable performance, and high working efficiency hydraulic components
2.Operator's station is designed for comfort and safety such as fully-adjustable, suspension-mounted operator's seat.

Applications of Road Roller YZ12H with Rexroth :
This Road Roller YZ12H with Rexroth is widely used to compress the surface being rolled to ensure a smooth, even result on the construction site such as road-making, runway of the airport, and building.

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length | 6000mm |
| 2 | Width(to outside of wheels) | 2300mm |
| 3 | Height(To the top of the cab) | 3055mm |
| 4 | Wheel base | 2945mm |
| 5 | Tread | 1560mm |
| 6 | Min. ground clearance | 395mm |
| Main Technical Specification |
| 1 | Static line force | 300N/cm |
| 2 | Dynamic line force | 1174 N/cm |
| 3 | Operating weight | 12000kg |
| 4 | Nominal Amplitude-high-low | 1.75mm 0.85mm |
| 5 | Centrifugal-Force-high-low | 250kN 125kN |
| 6 | Total stress force | 31500(kg) |
| 7 | Static Weight at Drum | 6500kg |
| 8 | Static Weight at Tires | 5500kg |
| 9 | Frequency | 31Hz |
| 10 | Min. turning radius(Outside of rear wheel) | 5880mm |
| 11 | Drum diameter | 1530mm |
| 12 | Drum width | 2130mm |
| 13 | Drum thickness | 25mm |
| 14 | Traveling speed(Km/h) |  |
|  | Stepless transmission | 0~12.1 |
| 15 | Gradient capacity | 20% |
| Diesel engine |
| 1 | Model | Dongfeng Cummins engine 6BT5.9-C150 |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 110 kW |
| 4 | Bore and stroke | 102X120mm |
| 5 | Total exhaust of cylinder | 5.9 (L) |
| 6 | Rated speed | 2200(r/min) |
| 7 | Max. Torque | 590(N.M)/1500RPM |
| 8 | Starting type | Electric |
| 9 | Min. specific fuel consumption | 229(g/Kw.h) |
| 10 | Net weight | 410±20(kg) |
| Driving System |
| 1 | Model | Static Hydraulic stepless driving |
| 2 | Type | Drive pump +drive motor + reducer |
| 3 | Model of drive pump | A4VG90HWDL1/32R |
| 4 | Model of drive motor | AA2FM80/61W |
| 5 | System pressure | 40MPa |
| 6 | Type of reducer | Spur gear parallel shaft constant-mesh |
| 7 | Gear ratio of reducer | 2.94 |
| Axle and Tire |
| 1 | Type of main reducer | spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 3.889 |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Gear of ratio of final reducer | 4.941 |
| 5 | Gear ratios | 19.2155 |
| 6 | Size of tire | 23.1-26-12PR |
| Working Device Hydraulic System |
| 1 | Model of tandem pump(vibrating +steering) | HP051B498BIJM20-7BRAB06-1 |
| 2 | Vibrating hydraulic system pressure | 160(kgf/cm2) |
| 3 | Model of oil motor | HM051A878BEP020-7 |
| 4 | Solenoid vibratory valve | ZF250B |
| Steering System |
| 1 | Type | Middle articulated frame. Full-hydraulic Steering |
| 3 | Model of redirector | BZZ1-E500C |
| 4 | System pressure | 12MPa |
| 5 | Dimension of steering cylinder | Ф90*45*280(mm) |
| Brake System |
| 1 | Type of traveling brake | Single chamber brake valve Caplier disc brake Air over oil activate rear axle |
| 2 | Air pressure | 6-8(kgf/cm2) |
| 3 | Type of parking brake | Hand brake Flexible shaft control clamp brake |
| Oil Capacity |
| 1 | Fuel(diesel) | 250 (L) |
| 2 | Engine lubricating oil | 15 (L) |
| 3 | Oil for gear box | 2.2(L) |
| 4 | Oil for hydraulic system | 200 (L) |
| 5 | driving axles(R) | Oil for main reducer | 18(L) |
|  |  | Oil for final reducer | 2X3(L) |
| 6 | Oil for brake system | 1.5( L) |
| 7 | Oil for vibrating drum | 2X56(L) |

The other construction machinery/construction equipment are available, such as wheel loaders, motor graders, backhoe loaders, etc.