## 8228-5 Single Drum Vibratory Roller

1. 8228-5 single drum vibratory roller offers two vibration frequencies and amplitudes to compact even the toughest roads.
2. Combination seals for leak-free performance
3. Driver cab delivers maximum comfort and safety. Adjustable cab seat is available with a suspension system. 
4. Soil density gauge allows vibratory roller operator to precisely control soil density.

Specifications of 8228-5 Single Drum Vibratory Roller :

| Model | 8228-5 |
| --- | --- |
| Length×Width×Height(mm) | 6460×2410×3335 |
| Operating weight(Kg) | 22000 |
| Nominal Vibration Amplitude high/low(mm) | 2.1/1.1 |
| Frequency(HZ) | 28/32 |
| Centrifugal-Force high/low(KN) | 390/270 |
| Gradient capacity (%) | 30 |
| Wheel base(mm) | 3150 |
| Diesel engine | ShangChai SC8D180.1G 2B1 |
| Rated output(KW) | 132 |

Changlin construction machinery/construction equipment: wheel loaders, road rollers, motor graders, backhoe loaders, pavers, Truck Mounted Crane, concrete truck mixers.