## 8108L Double Drum Vibratory Roller

1. Quality engine delivers great power, low emission and fuel consumption.
2. Mechanical drive powers the axle for traveling. Electro-hydraulic control provides two vibration amplitudes. Hydraulic steering hinge is another value-added feature to the vibratory roller. 
3. Two braking systems are used, including the hand brake and air-over-oil operated foot brake, for safety and reliability.
4. Compact design, curved hood with esthetic appeal. 
5. Airy driver’s cabin with optional air-conditioner for cooling and heating. 
6. Optional cam-driven vibrating drum for poweful compaction of cohesive soil.

Specifications of 8108L Double Drum Vibratory Roller:

| Model | 8108L |
| --- | --- |
| Length×Width×Height(mm) | 5500×2300×3000 |
| Operating weight(Kg) | 10000 |
| Nominal Vibration Amplitude high/low(mm) | 1.74/0.82 |
| Frequency(HZ) | 32 |
| Centrifugal-Force high/low(KN) | 198/93 |
| Gradient capacity (%) | 25 |
| Wheel base(mm) | 2900 |
| Diesel engine | Cummins 4BTA3.9-C100 |
| Rated output(KW) | 80 |

Changlin construction machinery/construction equipment: wheel loaders, road rollers, motor graders, backhoe loaders, pavers, Truck Mounted Crane, concrete truck mixers.