## 8206 Single Drum Vibration Roller

1. Hydraulic drive, vibration motor, and stepless speed controller are three main selling points of 8206 single drum vibration roller.
2. Vibration motor delivers vibration to the drum roller at one single frequency while offering two vibration amplitudes. This extra vibration allows a small, light vibratory roller to perform as well as a heavier one.
3. Reasonable configurations, reliable performance, high-efficiency hydraulic components. 
4. Electronic monitoring system and digital soil density gauge display real-time compaction result.

Specifications of 8206 Single Drum Vibration Roller :

| Model | 8206 |
| --- | --- |
| Length×Width×Height(mm) | 6298×2420×3210 |
| Operating weight(Kg) | 20000 |
| Nominal Vibration Amplitude high/low(mm) | 2.06/1.06 |
| Frequency(HZ) | 28/31 |
| Centrifugal-Force high/low(KN) | 390/253 |
| Gradient capacity (%) | 45 |
| Wheel base(mm) | 3100 |
| Diesel engine type | WeiChai engine WP6G 175E22 |
| Rated output(KW) | 129 |

Changlin construction machinery/construction equipment: wheel loaders, road rollers, motor graders, backhoe loaders, pavers, Truck Mounted Crane, concrete truck mixers.