## Road Roller YZK12HD with Rexroth

Structures of Road Roller YZK12HD with Rexroth :
1. Road Roller YZK12HD with Rexroth is equipped with DongFeng Cummins engine
2.Double frequency & Double amplitude and super centrifugal force creates strong compacting effect
3. PD model are comprised of 3 segments and are dismantled.
4. Hydrostatic travel and vibration drive, and stepless speed regulating.

Features of Road Roller YZK12HD with Rexroth :
1. Reasonable configuration, reliable performance, and high working efficiency hydraulic components
2.Operator's station is designed for comfort and safety such as fully-adjustable, suspension-mounted operator's seat.
Applications of Road Roller YZK12HD with Rexroth :
This Road Roller YZK12HD with Rexroth is widely used to compress the surface being rolled to ensure a smooth, even result on the construction site such as road-making, runway of the airport, and building.

Specifications of Road Roller YZK12HD with Rexroth :

| Overall Dimension |
| --- |
| 1 | Length | 6000mm |
| 2 | Width(to outside of wheels) | 2300mm |
| 3 | Height(To the top of the cab) | 3055mm |
| 4 | Wheel base | 2915mm |
| 5 | Tread | 1560mm |
| 6 | Min. ground clearance | 420mm |
| Main Technical Specification |
| 1 | Static line force(without PD) | 340N/cm |
| 2 | Dynamic line force(without PD) | 1300 N/cm |
| 3 | Operating weight | With PD | 13200kg |
|  |  | Without PD | 12100kg |
| 4 | Nominal Amplitude with PD | high | 1.45 mm |
|  |  | low | 0.7mm |
|  | Nominal Amplitude without PD | high | 1.8 |
|  |  | low | 0.9 |
| 5 | Centrifugal Force-high-low | At low frequency and high amplitude | 274kN |
|  |  | At high frequency and low amplitude | 171kN |
| 6 | Distribution weight of Drum | With PD | 8100kg |
|  |  | Without PD | 6980 kg |
| 7 | Distribution weight of Tyres | 5100kg |
| 8 | Frequency | 31/35Hz |
| 9 | Min. turning radius(Outside of rear wheel) | 5900mm |
| 10 | Drum dimension(with PD):Diameter X width X thickness | 1722×2100×28(mm) |
|  | Drumdimension(withoutPD):DiameterXwidth X thickness | 1530×2100×28(mm) |
| 11 | PD model specification | Number of pad feet | 135 |
|  |  | Area of one pad foot | 126cm2 |
|  |  | Height of pad feet | 80mm |
| 12 | Traveling speed(Km/h),3 forward &3 reverse |
|  | (1) 1st gear (F/R) | 0~4.8 |
|  | (2) 2nd gear (F/R) | 0~6.4 |
|  | (3) 3rd gear (F/R) | 0~10.6 |
| 13 | Gradient capacity | With PD | 30% |
|  |  | Without PD | 40% |
| Diesel engine |
| 1 | Model | DongFeng Cummins engine 6BTA5.9 |
| 2 | Type | Vertical, in-line, liquid-cooled and four-stroke engine |
| 3 | Rated output | 110 kW |
| 4 | Total exhaust of cylinder | 5.9 (L) |
| 5 | Rated speed | 2200(r/min) |
| 6 | Max. Torque | 590(N.M)/1500RPM |
| 7 | Starting type | Electric |
| 8 | Min. specific fuel consumption | 229(g/Kw.h) |
| 9 | Net weight | 430(kg) |
| Driving System |
| 1 | Model | Hydrostatic travel and vibration drive |
| 2 | Type | Drive pump +drive motor + reducer |
| 3 | Model of drive pump | A4VG71HWDL1/32R-NAF02F041D-S |
| 4 | Model of vibration driving motor +reducer Ratio of reducer | A6VE55EZ4/63W-VZL027B+GFT26T2 62 |
| 5 | Model of rear driving motor+ reducer Ratio of reducer | A6VM80EZ4/3W-VAB027B+EM1020/MR 3.08 |
| 6 | System pressure | 38MPa |
| Axle and Tire |
| 1 | Type of main reducer | spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 3.889 |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Gear of ratio of final reducer | 4.941 |
| 5 | Total ratios | 23.2584 |
| 6 | Rim model | DW20 |
| 7 | Size of tire | 23.1-26-12PR |
| Working Device Hydraulic System |
| 1 | Model of vibratory pump | A10VG45EZ2DM1/10R-NSC10F013D |
| 2 | System pressure | 280(kgf/cm2) |
| 3 | Model of vibratory motor | A10FM45/52W-VRC60N007 |
| Steering System |
| 1 | Type | Middle articulated frame. Full-hydraulic Steering |
| 2 | Model of steering pump | AZ-PF-1X/022RRRR20KB |
| 3 | Model of redirector | BZZ1-E500C |
| 4 | System pressure | 15MPa |
| 5 | Dimension of steering cylinder | Ф90*45*280(mm) |
| Brake System |
| 1 | Type of traveling brake | traveling brake depend on static hydraulic tow of close-circuit system. vibratory reducer with a brake which control by a solenoid valve. |
| 2 | Type of parking brake | Hand brake Flexible shaft control clamp brake |
| Oil Capacity |
| 1 | Fuel(diesel) | 250 (L) |
| 2 | Engine lubricating oil | 15 (L) |
| 3 | Oil for hydraulic system | 140 (L) |
| 4 | Oil for driving axles(F/R) | 24 (L) |
| 5 | Oil for vibrating drum | 2X56(L) |
| 6 | Reducer(EM1020/MR/3.08) | 2.2L |

Wheel loaders, motor graders, pavers, Truck Mounted Crane and other construction machinery and construction equipment are provided.