## 275 Skid Steer Loader

275 Skid Steer Loader Specifications
Equipped with reliable Perkins engine
Bucket automatic leveling ability

Double handles control loading and traveling, easy & reliable operating

| Overall Dimension |
| --- |
| 1 | Length(with bucket on ground) | 3550(mm) |
| 2 | Width(to outside of wheels) | 1800(mm) |
| 3 | Bucket width | 1890(mm) |
| 4 | Height(To the top of the cab) | 2020(mm) |
| 5 | Wheel base | 1110(mm) |
| 6 | Tread | 1494(mm) |
| 7 | Min. ground clearance | 220(mm) |
| Main Technical Specification |
| 1 | Rated load | 950(Kg) |
| 2 | Operating weight | 3500KG |
| 3 | Rated bucket capacity | 0.53(m3) |
| 4 | Max. breakout force | 27kN |
| 5 | Static tipping loads | ≥20kN |
| 6 | Max. dump clearance | 2326(mm) |
| 7 | Dump reach | 785(mm) |
| 8 | Dump angle at any position | ≥40° |
| 9 | Angle of departure | 30° |
| 10 | Digging depth(with bucket bottom horizontal) | 0(mm) |
| 11 | Min. turning radius |
|  | (1)Outside of bucket | 2290(mm) |
|  | (2)Outside of front wheel | 1307(mm) |
|  | (3)outside of frame tail | 1540 (mm) |
| 12 | Lifting time of bucket | ≤4.2(sec.) |
| 13 | Lowering time of bucket | ≤2.5(sec.) |
| 14 | Dumping time | ≤2.6(sec.) |
| 15 | Traveling speed(Km/h),1forward and 1 reverse |
|  | (1)forward gear | 0~12 |
|  | (2)reverse gear | 0~12 |
| Diesel engine |
| 1 | Model | Perkins 804D-33T 804D-33T |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 55 (kW) |
| 4 | No-bore of cylinder/stroke | 4-94×120 (mm) |
| 5 | Total exhaust of cylinder | 3.3 (L) |
| 6 | Voltage of starting moto | 12(V) |
| 7 | Rated speed | 2500(r/min) |
| 8 | Max. Torque | 245(N.M)/1600rpm |
| 9 | Starting type | Electric |
| 10 | Net weight | 265(kg) |
| Power train |
| Driving system |
| 1 | Model | Hydrostatic four wheel drive |
| 2 | Type | Driving pump+traveling motor+Chain driving |
| 3 | Model of driving pump | MPT046C-BA |
| 4 | Model of driving motors | MS06(French POCLAIN) |
| 5 | Type of chain driving | Double row chain driving |
| 6 | Ratio of chain driving | 30:11 |
| 7 | Model of chain | 20A-1X64 20A-1X50 |
| 8 | Size of tire | 12-16.5NHS-10PR L-2B |
| 9 | Charge pressure | 24.8bar |
| 9 | System pressure | 30MPa |
| Working Device Hydraulic System |
| 1 | Model of oil pump | WP15A1B330R05KA147N (Italian CASAPPA) |
| 2 | System pressure | 21MPa |
| 3 | Model of distribution valve | SDM141 ( Italian WALVOIL) |
| 4 | Model of Leveling valve | V-VCFL (Italian WALVOIL) |
| 5 | (D*L)Dimension of lifting cylinder | Ф80*40*838(mm) |
| 6 | (D*L)Dimension of tilting cylinder | Ф80*35*371(mm) |
| Brake System |
| 1 | Type of traveling brake | Traveling brake depend on static hydraulic tow of close-circuit hydraulic system |
| 2 | Type of parking brake | Traveling motors within brake actuated via operating solenoid valve |
| Oil Capacity |
| 1 | Fuel(diesel) | 83(L) |
| 2 | Engine lubricating oil | 10(L) |
| 3 | Oil for chain box(one side) | 5.7(L) |
| 4 | Oil for hydraulic system | 50(L) |