## Wheel Loader 937H

1. The 937H Wheel Loader is equipped with Dongfeng Cummins Engine.
2. This Wheel loader adopts 3 forward and 3 reverse power shift transmission.
3. The combined seal cylinder adopted by this wheel loader obtains high seal performance and more reliability.

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length (with bucket on ground) | 6920(mm) |
| 2 | Width (to the outside of wheels) | 2305(mm) |
| 3 | Bucket width | 2430(mm) |
| 4 | Height (to the top of the cab) | 3151(mm) |
| 5 | Wheel base | 2750(mm) |
| 6 | Tread | 1855(mm) |
| 7 | Min. ground clearance | 360(mm) |
| Main Technical Specification |
| 1 | Rated load | 3000(Kg) |
| 2 | Operating weight | 10200KG |
| 3 | Rated bucket capacity | 1.7(m3) |
| 4 | Max. breakout force | 96kN |
| 5 | Max. dump clearance | 2934(mm) |
| 6 | Dump reach | 1043(mm) |
| 7 | Dump angle at any position | ≥45° |
| 8 | Min. turning radius |
|  | (1) Outside of bucket | 5600(mm) |
|  | (2) Outside of rear wheel | 5205(mm) |
| 9 | Pivot angle frame | 38+1° |
| 10 | Oscillating angle of rear axle | +11° |
| 11 | Lifting time of bucket | ≤5.1(sec.) |
| 12 | Lowering time of bucket | ≤3.0(sec.) |
| 13 | Dumping time | ≤1.1(sec.) |
| 14 | Traveling speed (Km/h), 3 forward and 3 reverse |
|  | (1) 1st gear forward | 7.3 |
|  | (2) 2nd gear forward | 15.7 |
|  | (3) 3rd gear forward | 35 |
|  | (1) 1st gear reverse | 7.8 |
|  | (2) 2nd gear reverse | 16.8 |
|  | (3) 3rd gear reverse | 36 |
| Diesel Engine |
| 1 | Model | Dongfeng Cummins 6BT5.9-C120 |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 97(KW) |
| 4 | Inter-bore of cylinder / stroke | 102/120 (mm) |
| 5 | Total exhaust of cylinder | 5.9 (L) |
| 6 | Voltage of starting motor | 24(V) |
| 7 | Rated speed | 2200(r/min) |
| 8 | Max. torque | 440(N.M)/1500rpm |
| 9 | Starting type | Electric |
| 10 | Min. specific fuel consumption | 220(g/Kw.h) |
| Transmission System |
| 1. Torque Converter |
| 1 | Model | YJH315A-4 (Shanxi Aerospace Power) |
| 2 | Type | 3-elements. Single stage |
| 3 | Torque ratio | 3.1 |
| 4 | Cooling type | Pressure oil circulating |
| 2. Transmission Case |
| 1 | Model | Chinese Changlin |
| 2 | Type | Power shift, spur gear constantly in mesh |
| 3 | Gear shift position | 3 forward and 3 reverse gears |
| 3. Axle and Tire |
| 1 | Type of main reducer | Spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 3.889 |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Gear ratio of final reducer | 4.941 |
| 5 | Total ratios | 19.216 |
| 6 | Max. drawing force | 83kN |
| 7 | Size of tire | 17.5-25-12PR |
| Working Device Hydraulic System |
| 1 | Model of oil pump | CBGj2100 (SAE) |
| 2 | System pressure | 160(kgf/cm2) |
| 3 | Model of multichannel conversion valve | GDF32D2 |
| 4 | (D×L) Dimension of lifting cylinder | Ф125×70×697(mm) |
| 5 | (D×L) Dimension of tilt cylinder | Ф150×70×470(mm) |
| Steering System |
| 1 | Type | Middle articulated frame. Full-Hydraulic steering |
| 2 | Model of steering pump | CBG2050 (SAE) |
| 3 | Model of steering gear | BZZ1-E400C+FKA-143020 |
| 4 | Model of single-channel stable shunt valve | FLD-D30H |
| 5 | System pressure | 14MPa |
| 6 | Dimension of steering cylinder | Ф70×40×357(mm) |
| Brake System |
| 1 | Type of traveling brake | Air assisted oil.4 wheel brake |
| 2 | Air pressure | 7-8(kgf/cm2) |
| 3 | Type of emergency brake | Automatic cutting air brake |
| 4 | Type of parking brake | Drum brake Manual control cutting off air brake |
| Oil Capacity |
| 1 | Fuel (diesel) | 130(L) |
| 2 | Engine lubricating oil | 13.5(L) |
| 3 | Oil for converter and gear box | 35(L) |
| 4 | Oil for hydraulic system | 120(L) |
| 5 | Oil for driving axles (F/R) | 16/15(L) |

Changlin Construction Machinery (Engineering Vehicle/ construction equipment), High Quality!!